Pioneer CAC-Vxxx CD Autochangers comprehension guide
# Document revisions
Date (M/D/Y)	Author	Version	Description/Updates
04/02/2020	DJ	V1.0.0	Initial release
07/29/2020	DJ	V1.0.1	Better presentation & explanations, fixed some typo.
09/04/2020	DJ	V1.0.2	Add caution for shipping screws.
09/24/2020	DJ	V1.0.3	Add serialcheck.sh toolscript
10/01/2020	DJ	V1.0.4	Compacting

Note: If your device’s model name begins with DRM-xxxx, it’s a SCSI CD/DVD changer. This is beyond the scope of this document.
# Not usable easily
As you have guess theses CD autochangers (or can be also named “jukeboxes”) are not autonomous and user friendly. They are entirely controlled by a computer with an old school serial connection (RS-232C or RS-442A). So first, you need a cable to connect it to your computer.
# Manuals
Please read the original PDF user manual according to your model, they are available in this GitHub repository. Have a look to understand how they works, like loading & removing discs.

Note: For the CAC-V3000/3200 models: please be sure to set the left CD player address at number 1. Check user manual at chapter “PLAYER ADDRESS SETTING MODE” (page n°14/44).
Caution! Some models has shipping screws included to lock the carriage assy for transport. Please be sure to REMOVE them (if installed)
BEFORE POWERING ON the device!
# No serial port on your computer?
Serial ports or not really used anymore and had been replaced by USB. If you don’t have one you can buy an RS232-USB adapter (like FTDI FT232 or Prolific PL2303) on eBay, Amazon, AliExpress... (about 10€).
Note: The V5000 model is RS-422A, be sure to purchase a RS422-USB adapter!
# The cable
The needed cable depends on model you have.
For CAC-V180M and V5000 models, use a standard D-Sub DE-9 female (computer side) to D-Sub DE-9 male (CAC side) straight type cable. This kind of generic cable can be bought on Internet like eBay, AliExpress, Amazon, etc.... Do not use a Null-Modem (crossed) type cable, it will not work.

For CAC-V3000/3200 models: You have to build your own cable. Simply because these models requires a DA15 connector (not used in regular computing). Here is the schema (check user manual for RS-422A):

Parts:
- a female DE-9 connector (for computer side)
- a male DA-15 connector (for autochanger side)
- standard microphone XLR cable (3 poles for GND, RX, TX)
- soldering stuff and skills
# Test your connection
Connect your serial cable and power on the autochanger.
## With Linux
I created a tiny interactive shell script in Bash (serialcheck.sh) to easily test the jukebox good connection. Download-it and run-it in a terminal.
The script shows you the detected serial ports list. Answer questions and that’s it.
jonathan@dellpioneer:~$ bash /opt/ccc/tools/serialcheck.sh
Welcome to CCC autochanger serial checker script v1 for Linux.

This tiny script is interactive and will ask you some questions.
Listing serial ports... 7 found.

Device | Physical port
------ | -------------
ttyS0 | /devices/platform/serial8250/tty/ttyS0
ttyS1 | /devices/platform/serial8250/tty/ttyS1
ttyS2 | /devices/platform/serial8250/tty/ttyS2
ttyS3 | /devices/platform/serial8250/tty/ttyS3
ttyUSB0 | /devices/pci0000:00/0000:00:1d.0/usb2/2-1/2-1.2/2-1.2:1.0/ttyUSB0/tty/ttyUSB0
ttyUSB1 | /devices/pci0000:00/0000:00:1d.0/usb2/2-1/2-1.3/2-1.3:1.0/ttyUSB1/tty/ttyUSB1
ttyUSB2 | /devices/pci0000:00/0000:00:1d.0/usb2/2-1/2-1.4/2-1.4:1.0/ttyUSB2/tty/ttyUSB2

Please select a serial port:
1) ttyS0
2) ttyS1
3) ttyS2
4) ttyS3
5) ttyUSB0
6) ttyUSB1
7) ttyUSB2
#? 5
You have chosen ttyUSB0.
Please select an autochanger model:
1) CAC-V180M
2) CAC-V3000/V3200/V5000
#? 1
You have chosen CAC-V180M.
Speed set to 4800bps.
Applying stty settings... OK.
Trying to communicate with the autochanger...
Command '?X' send! Waiting for reply...
Congratulations! Your autochanger answered correctly with 'P150904'.
Do you want to send custom commands (manual mode) now? Y(es) or N(o)
Manual mode entered. Type your command and press Enter (for each one).
Warning: All chars will be sent as is! There is no verification.
Type 'exit' to terminate this program.
Command: ?Z
Command '?Z' send!
XXX
Command: ?P
Command '?P' send!
P20
Command: exit
Manual mode exited.
Goodbye.
jonathan@dellpioneer:~$

## With Windows
### Port detection
Serial ports can be listed with the “Device Manager”.
On Windows serial ports are labeled COM followed by a number.

### Check usability
Download & install CompuPhase Termite program (very simple to use & easy for communicate with our Pioneer jukeboxes). Open Termite and go to settings.

- Select your serial port number (COM1, COM2, COM…)
- Baud rate = 4800 or 9600 (according to autochanger models & settings)
- Data bits = 8
- Stop bits = 1
- Parity = none
- Flow control = none
- Forward = none
- Please sure to be connected
### Final transmission tests
- For CAC-V3000/V3200/V5000 models:
  - Type “1PS!!” (without the quotes) in the bottom text zone and press Enter. Confirm that the Pioneer jukebox re-initialize itself.
  - Now type “1PS1ZS” (without the quotes) in the bottom text zone and press Enter. Confirm that the Pioneer jukebox tries to load disc n°1.
- For CAC-V180M model:
  - Type “!!” (without the quotes) in the bottom text zone and press Enter. Confirm that the Pioneer returns “E04”.
  - Type “1ZS” (without the quotes) in the bottom text zone and press Enter. Confirm that the Pioneer jukebox tries to load disc n°1.

# Controller/commands (programming)
As you have guessed, you have to dialogue with ASCII text commands to control your changer. Obviously it’s a raw way to use it. In the past a lot of owners programmed themselves a controller software according for their usage with C, Pascal, BASIC or Visual Basic languages. Few professional and user friendly commercial software existed but no one has leaked nowadays.

Programming manuals are available in the /programming directory on the GitHub repo.